## Slide 1: Titolo presentazione sottotitolo
Milano, XX mese 20XX
Wireless and Mobile Propagation
Prof. Michele D’Amico
Politecnico di Milano
2025

## Slide 2: Private Mobile Radio Network Design
Iman Javaheri
Peyman Javaheri
Hamed Lotfalizadeh

## Slide 3: Outline
Introduction
Network Architecture
VHF Side Design (Repeaters and Terminals)
Microwave Network Design
Repeater Placement & Coverage
Link Analysis & Coverage
Conclusion
Future Work

## Slide 4: Introduction
PMR for emergency/security services
Area: 100 km x 100 km, centered on Mashhad, Iran
Objective: High coverage, low cost, reliable links

## Slide 5: Project Goals
Minimize repeater count
Maximize coverage with LOS placement
Ensure microwave connectivity between repeaters
Simulate and validate with RadioMobile

## Slide 6: Network Architecture
Dual-network:
  VHF (158 MHz) for users ↔ repeaters
  Microwave (10–15 GHz) for repeater ↔ repeater

## Slide 7: Equipment Specs (VHF Side)
Repeaters: Motorola SLR5500 (50 W, 0.22 µV sensitivity)
Terminals: Motorola DM4000e (35 W, 0.3 µV sensitivity)
Antennas: Omni 5 dBi (repeater), 0 dBi (vehicle)
Repeater Antenna
Repeater
Terminal

## Slide 8: Microwave Network Design
P2P microwave links between repeaters
10 GHz: 25–70 km, 44.3 dBi gain antenna,10 m tower
15 GHz: 10–25 km, 41.4 dBi

## Slide 9: Repeater Placement Strategy
High elevation (>2000 m) for better LOS
4 repeaters placed manually

## Slide 10: Individual Coverage Plots
RPTR 1
RPTR 2
RPTR 3
RPTR 4

## Slide 11: Combined Coverage
Achieved 99.9% coverage

## Slide 12: Link Analysis
clear LoS
RPTR 1 – RPTR 2

## Slide 13: Network Quality Report
reflects the strength of the connection between pairs of repeaters
all links > 50 → strong and reliable

## Slide 14: Link Topologies
a. Full Mesh
b. Ring I
c. Line
d. Ring II

## Slide 15: Conclusion and Future Work
4-repeaters = 99.9% area coverage
Reliable microwave interconnect
Efficient, cost-effective PMR design
Future work:
Green energy: solar-powered repeaters

## Slide 16: Thank you for your attention!